Building an SPI Device Driver

---
Authors and license
Authors
Michael Welling
QWERTY Embedded Design, LLC
www.qwertyembedded.com
License
Creative Commons Attribution – Share Alike 4.0
https://creativecommons.org/licenses/by-sa/4.0/

---
What is SPI?
SPI (Serial Peripheral Interface) is a full duplex synchronous serial master/slave bus interface.
De facto standard first developed at Motorola in the 1980s.
A SPI bus consists of a single master device and possibly multiple slave devices.
Typical device interface
SCK – serial clock
MISO – master in slave out
MOSI – master out slave in
CSn / SSn – chip select / slave select
IRQ / IRQn – interrupt

---
What is SPI?
SPI Master
SPI Slave
SCK
SCK
MOSI
MOSI
MISO
MISO
CSn
CSn0
CSn1
CSn
CSn2
CSn

---
Example SPI devices
Analog converters (ADC, DAC, CDC)
Sensors (inertial, temperature, pressure)
Serial LCD
Serial Flash
Touchscreen controllers
FPGA programming interface

---
SPI Modes
SPI Mode is typically represented by (CPOL, CPHA) tuple
CPOL – clock polarity
0 = clock idles low
1 = clock idles high
CPHA – clock phase
0 = data latched on falling clock edge, output on rising
1 = data latched on rising clock edge, output on falling
Mode (0, 0) and (1, 1) are most commonly used.
Sometimes listed in encoded form 0-3.

---
SPI Modes

---
Linux SPI Subsystem
First developed in early 2000s (2.6 ERA) based on the work of several key developers in including:
David Brownell
Russell King
Dmitry Pervushin
Stephen Street
Mark Underwood
Andrew Victor
Vitaly Wool

---
Linux SPI Subsystem
Past maintainers of the Linux SPI subsystem:
David Brownell
Grant Likely
Current maintainer:
Mark Brown

---
Linux SPI Mailinglist
List: linux-spi; ( subscribe / unsubscribe )
Info:
This is the mailing list for the Linux SPI subsystem.
Archives:
http://marc.info/?l=linux-spi
Footer:
---
To unsubscribe from this list: send the line "unsubscribe linux-spi" in
the body of a message to majordomo@vger.kernel.org
More majordomo info at http://vger.kernel.org/majordomo-info.html

---
Controller Drivers
Controller drivers are used to abstract and drive transactions on an SPI master.
The host SPI peripheral registers are accessed by callbacks provided to the SPI core driver. (drivers/spi/spi.c)
struct spi_controller

---
Controller Drivers
Allocate a controller
spi_alloc_master()
Set controller fields and methods
mode_bits - flags e.g. SPI_CPOL, SPI_CPHA, SPI_NO_CS,
SPI_CS_HIGH, SPI_RX_QUAD, SPI_LOOP
.setup() - configure SPI parameters
.cleanup() - prepare for driver removal
.transfer_one_message()/.transfer_one() - dispatch one msg/transfer (mutually exclusive)
Register a controller
spi_register_master()

---
Controller Devicetree Binding
The SPI controller node requires the following properties:
- compatible - Name of SPI bus controller following generic names recommended practice.
In master mode, the SPI controller node requires the following additional properties:
- #address-cells - number of cells required to define a chip select address on the SPI bus.
- #size-cells - should be zero.
Optional properties (master mode only):
- cs-gpios	- gpios chip select.
- num-cs	- total number of chipselects.
So if for example the controller has 2 CS lines, and the cs-gpios
property looks like this:
cs-gpios = <&gpio1 0 0>, <0>, <&gpio1 1 0>, <&gpio1 2 0>;

---
Controller Devicetree Binding
Example:
spi1: spi@481a0000 {
        compatible = "ti,omap4-mcspi";
        #address-cells = <1>;
        #size-cells = <0>;
        reg = <0x481a0000 0x400>;
        interrupts = <125>;
        ti,spi-num-cs = <2>;
        ti,hwmods = "spi1";
        dmas = <&edma 42 0
        &edma 43 0
        &edma 44 0
        &edma 45 0>;
        dma-names = "tx0", "rx0", "tx1", "rx1";
        status = "disabled";
        };

---
Protocol Drivers
For each SPI slave you intend on accessing, you have a protocol driver. SPI protocol drivers can be found in many Linux driver subsystems (iio, input, mtd).
Messages and transfers are used to communicate to slave devices via the SPI core and are directed to the respective controller driver transparently.
A struct spi_device is passed to the probe and remove functions to pass information about the host.

---
Protocol Drivers
Transfers
A single operation between master and slave
RX and TX buffers pointers are supplied
Option chip select behavior and delays
Messages
Atomic sequence of transfers
Argument to SPI subsystem read/write APIs

---
struct spi_device
struct spi_device {
struct device dev;
struct spi_controller * controller;
struct spi_controller * master;
u32 max_speed_hz;
u8 chip_select;
u8 bits_per_word;
u16 mode;
int irq;
void * controller_state;
void * controller_data;
char modalias;
int cs_gpio;
struct spi_statistics statistics;
};
Controller side proxy for an SPI slave device. Passed to the probe and remove functions with values based on the host configuration.

---
struct spi_device
#define	SPI_CPHA	0x01	/* clock phase */
#define	SPI_CPOL	0x02	/* clock polarity */
#define	SPI_MODE_0	(0|0)	/* (original MicroWire) */
#define	SPI_MODE_1	(0|SPI_CPHA)
#define	SPI_MODE_2	(SPI_CPOL|0)
#define	SPI_MODE_3	(SPI_CPOL|SPI_CPHA)
#define	SPI_CS_HIGH	0x04	/* chipselect active high? */
#define	SPI_LSB_FIRST	0x08	/* per-word bits-on-wire */
#define	SPI_3WIRE	0x10	/* SI/SO signals shared */
#define	SPI_LOOP	0x20	/* loopback mode */
#define	SPI_NO_CS	0x40	/* 1 dev/bus, no chipselect */
#define	SPI_READY	0x80	/* slave pulls low to pause */
#define	SPI_TX_DUAL	0x100	/* transmit with 2 wires */
#define	SPI_TX_QUAD	0x200	/* transmit with 4 wires */
#define	SPI_RX_DUAL	0x400	/* receive with 2 wires */
#define	SPI_RX_QUAD	0x800	/* receive with 4 wires */

---
Probe Function
static int myspi_probe(struct spi_device *spi)
{
struct myspi	*chip;
struct myspi_platform_data	*pdata, local_pdata;
...
}

---
Probe Function
static int myspi_probe(struct spi_device *spi)
{
...
match = of_match_device(of_match_ptr(myspi_of_match), &spi->dev);
if (match) {
/* parse device tree options */
pdata = &local_pdata;
...
}
else {
/* use platform data */
pdata = &spi->dev.platform_data;
if (!pdata)
return -ENODEV;
}
...
}

---
Probe Function
static int myspi_probe(struct spi_device *spi)
{
...
/* get memory for driver's per-chip state */
chip = devm_kzalloc(&spi->dev, sizeof *chip, GFP_KERNEL);
if (!chip)
return -ENOMEM;
spi_set_drvdata(spi, chip);
...
return 0;
}

---
OF Device Table
Example:
static const struct of_device_id myspi_of_match[] = {
{
.compatible = "mycompany,myspi",
.data = (void *) MYSPI_DATA,
},
{ },
};
MODULE_DEVICE_TABLE(of, myspi_of_match);

---
SPI Device Table
Example:
static const struct spi_device_id myspi_id_table[] = {
{ "myspi", MYSPI_TYPE },
{ },
};
MODULE_DEVICE_TABLE(spi, myspi_id_table);

---
struct spi_driver
struct spi_driver {
const struct spi_device_id * id_table;
int (* probe) (struct spi_device *spi);
int (* remove) (struct spi_device *spi);
void (* shutdown) (struct spi_device *spi);
struct device_driver driver;
};

---
struct spi_driver
Example:
static struct spi_driver myspi_driver = {
        .driver = {
        .name = "myspi_spi",
        .pm = &myspi_pm_ops,
        .of_match_table = of_match_ptr(myspi_of_match),
        },
        .probe = myspi_probe,
        .id_table = myspi_id_table,
};
module_spi_driver(myspi_driver);

---
Kernel APIs
spi_async()
asynchronous message request
callback executed upon message complete
can be issued in any context
spi_sync()
synchronous message request
may only be issued in a context that can sleep (i.e. not in IRQ context)
wrapper around spi_async()
spi_write()/spi_read()
helper functions wrapping spi_sync()

---
Kernel APIs
spi_read_flash()
Optimized call for SPI flash commands
Supports controllers that translate MMIO accesses into standard SPI flash commands
spi_message_init()
Initialize empty message
spi_message_add_tail()
Add transfers to the message’s transfer list

---
Slave Node Devicetree Binding
SPI slave nodes must be children of the SPI controller node.
In master mode, one or more slave nodes (up to the number of chip selects) can
be present.
Required properties are:
- compatible - Name of SPI device following generic names recommended practice.
- reg - Chip select address of device.
- spi-max-frequency - Maximum SPI clocking speed of device in Hz.

---
Slave Node Devicetree Binding
All slave nodes can contain the following optional properties:
- spi-cpol - Empty property indicating device requires inverse clock polarity (CPOL) mode.
- spi-cpha - Empty property indicating device requires shifted clock phase (CPHA) mode.
- spi-cs-high - Empty property indicating device requires chip select active high.
- spi-3wire - Empty property indicating device requires 3-wire mode.
- spi-lsb-first - Empty property indicating device requires LSB first mode.
- spi-tx-bus-width - The bus width that is used for MOSI. Defaults to 1 if not present.
- spi-rx-bus-width - The bus width that is used for MISO. Defaults to 1 if not present.
- spi-rx-delay-us - Microsecond delay after a read transfer.
- spi-tx-delay-us - Microsecond delay after a write transfer.

---
Slave Node Devicetree Binding
Example:
&spi1 {
#address-cells = <1>;
#size-cells = <0>;
status = "okay";
pinctrl-names = "default";
pinctrl-0 = <&spi1_pins>;
myspi@0 {
compatible = "mycompany,myspi";
spi-max-frequency = <2000000>;
spi-cpha;
...
reg = <0>;
};
...
};

---
Platform Registration
struct spi_board_info {
char modalias;
const void * platform_data;
const struct property_entry * properties;
void * controller_data;
int irq;
u32 max_speed_hz;
u16 bus_num;
u16 chip_select;
u16 mode;
};

---
Platform Registration
Example:
static struct spi_board_info myspi_board_info[] = {
        {
        .modalias = "myspi",
        .platform_data = &myspi_info,
        .irq = MYIRQ,
        .max_speed_hz = 2000000,
        .chip_select = 2,
  …..
        },
 };

---
Baconbits SPI Hardware

---
Questions?

---
Thank you!