Introduction to
Linux Kernel Modules
and Kbuild

---
What the heck is a kernel module?

---
What is a kernel module?
- A way to dynamically add code (or data) to a running kernel
- Subsequently to optionally remove that same code
- A way to automatically load only the drivers we need
- A way to provide a choice between multiple modular drivers
- A way to architect kernel code in a modular way

---
Aren’t modules and drivers the same thing?
- While most drivers are written as modules
- Not all modules are drivers
- A kernel module is the simplest way of adding a payload of bytes to the kernel (whether code or data)
- A module can implement a driver, or library code, or a kprobe, or whatever you can dream up you want to add to a kernel...

---
A Simple module
- Static functions
- Return codes
- module_init()
- module_exit()
- __init attribute
- __exit attribute
#include <linux/module.h>
#include <linux/init.h>
static int __init my_init(void)
{
        pr_info("Hello: module loaded at 0x%p\n", my_init);
        return 0;
}
static void __exit my_exit(void)
{
        pr_info("Bye: module unloaded from 0x%p\n", my_exit);
}
module_init(my_init);
module_exit(my_exit);
MODULE_AUTHOR("A GENIUS");
MODULE_LICENSE("GPL v2");
NOTE: Output edited for brevity

---
The anatomy of a module (ELF file)
$ arm-linux-gnueabihf-objdump -x trivial.ko
1 .text 00000000 00000000 00000000 00000058 2**0
CONTENTS, ALLOC, LOAD, READONLY, CODE
2 .init.text 00000030 00000000 00000000 00000058 2**2
CONTENTS, ALLOC, LOAD, RELOC, READONLY, CODE
3 .exit.text 00000024 00000000 00000000 00000088 2**2
CONTENTS, ALLOC, LOAD, RELOC, READONLY, CODE
9 .rodata.str1.4 00000042 00000000 00000000 00000138 2**2
CONTENTS, ALLOC, LOAD, READONLY, DATA
11 .data 00000000 00000000 00000000 00000180 2**0
CONTENTS, ALLOC, LOAD, DATA
NOTE: Output edited for brevity

---
__Init code and __initdata
static int some_data __initdata = 1 ;
void __init somefunc (void) { ... }
[0.841689] Freeing unused kernel memory: 424k freed
NOTE: Output edited for brevity

---
Modules and licensing
License	Meaning	Tainted
GPL	GNU Public License V2 or later	No
GPL v2	GNU Public License V2	No
GPL and additional rights	GNU Public License V2 rights and more	No
Dual BSD/GPL	GNU Public License V2 or BSD License	No
Dual MPL/GPL	GNU Public License V2 or MPL License	No
Dual MIT/GPL	GNU Public License V2 or MIT License	No
Proprietary	Not GPL compatible	Yes

---
Taint bits
#define TAINT_WARN	9
#define TAINT_CRAP	10
#define TAINT_FIRMWARE_WORKAROUND 11
#define TAINT_OOT_MODULE	12
#define TAINT_UNSIGNED_MODULE	13
#define TAINT_SOFTLOCKUP	14
#define TAINT_LIVEPATCH	15
#define TAINT_AUX	16
#define TAINT_PROPRIETARY_MODULE	0
#define TAINT_FORCED_MODULE	1
#define TAINT_CPU_OUT_OF_SPEC	2
#define TAINT_FORCED_RMMOD	3
#define TAINT_MACHINE_CHECK	4
#define TAINT_BAD_PAGE	5
#define TAINT_USER	6
#define TAINT_DIE	7
#define TAINT_OVERRIDDEN_ACPI_TABLE 8
NOTE: Output edited for brevity

---
Exporting Symbols
- The kernel has an in-kernel linker
- All symbols are considered static by default
- You must explicitly export symbols with EXPORT_SYMBOL()
- You can also elect to EXPORT_SYMBOL_GPL()
- Or use EXPORT_SYMBOL_GPL_FUTURE()
- There are also other EXPORT_SYMBOL_* macros

---
KBuild
- The kernel build system is called Kbuild
- Sub directories have simple Makefiles
- Simple configuration system called Kconfig
- Graphical menuconfig (and others) for Kconfig
- Most other embedded code bases use it

---
KBuild
.config
  CONFIG_FOO=m ← Configure foo as module
Makefile
  obj-$(CONFIG_FOO) += foo.o	← module/builtin
  obj-y += bar.o	← builtin
  obj-$(CONFIG_BLAH) += blah/	← Subdirectory

---
KConfig
- A language to describe configuration options for Kbuild
- Attributes of type, defaults, help, dependencies, selects, conditionals

---
KConfig
config FOO
    tristate “one line description of config option”
    default m
    depends BLAH
    select FLOOP
    select BAR if !BAZ
    help
      This is a multiline long help.

---
menuconfig

---
Menuconfig
- Up/Down moves through selections
- Left/Right moves through bottom selections
- Enter goes into “→” subdirectories
- Space toggles values
- Y/N/M allows you to choose values
- “/” allows to search options by name

---
Bulding a module in tree
- Add your code into the tree
- Add yourself to Kconfig
- Add configuration to .config with menuconfig
- make will then build the kernel and your module

---
Bulding a module out-of-tree
- KROOT=/path/to/relevant/kernel/headers
- make -C $KROOT M=$(pwd) modules
- Use the make system in $KROOT
- Build the modules in the local directory

---
Cross compiling a module
- Set ARCH to the architecture you want to build
- Set CROSS_COMPILE to the compiler triplet
make -C $ROOT M=$(pwd) ARCH=arm \
        CROSS_COMPILE=arm-linux-gnueabihf- modules

---
Installing a module
Copies a module to /usr/modules/$(uname -r)
make -C $ROOT M=$(pwd) ARCH=arm modules_install

---
insmod
- Insert a module into a running kernel
- Invokes the in-kernel linker to link the module into the kernel using the kernel symbol table
$ sudo insmod /path/to/modulename.ko <options>
Modules are files with the modulename ending in .ko

---
lsmod
- List currently loaded modules
- Top module was most recently loaded
- Lists size, reference count, and optional dependencies
debian@beaglebone:~$ lsmod
Module Size Used by
Evdev 13811 1
uio_pdrv_genirq 4205 0
uio 11036 1 uio_pdrv_genirq
usb_f_mass_storage 51462 2

---
rmmod
- Remove a module by name (not filename)
- You can remove more than one module at a time, but the order matters if there are dependencies
$ rmmod foo
$ rmmod bar blah

---
depmod
Builds dependency files for all modules used by modprobe
        $ ls -1 /lib/modules/$(uname -r)
        modules.alias
        modules.builtin
        modules.dep
        modules.order
        modules.symbols

---
modprobe
- A “smart” insmod
- Will load module pre-dependencies
- Allows you to set persistent options (and more)
- Uses /etc/modprobe.conf and /etc/modprobe.d
- Used by udevd to load drivers

---
Modprobe configuration
/etc/modprobe.d/foo.conf
        blacklist bar
        options blah option1=value option2=value … alias genericname foo

---
modinfo
Shows module metadata
root@beaglebone:~# modinfo uio
filename: /lib/modules/4.9.82-ti-r102/kernel/drivers/uio/uio.ko
license: GPL v2
depends:
intree: Y
vermagic: 4.9.82-ti-r102 SMP preempt mod_unload \
        modversions ARMv7 p2v8

---
dmesg
- dmesg shows kernel in-memory log buffer.
- Using the “-w” option does a “tail” of the log
root@beaglebone:~# dmesg -w

---
Questions?

---
Thank you!