Introduction to Linux kernel driver programming + i2c drivers

---
Introduction to Linux kernel driver programming: i2c drivers
The Linux kernel device model

---
Authors and license
- Authors
  - Michael Opdenacker
    Founder of Bootlin (formerly Free Electrons),
    kernel and embedded Linux engineering company
    https://bootlin.com/company/staff/michael-opdenacker
- License
  - Creative Commons Attribution – Share Alike 4.0
    https://creativecommons.org/licenses/by-sa/4.0/

---
Need for a device model
- For the same device, need to use the same device driver on multiple CPU architectures (x86, ARM…), even though the hardware controllers are different.
- Need for a single driver to support multiple devices of the same kind.
- This requires a clean organization of the code, with the device drivers separated from the controller drivers, the hardware description separated from the drivers themselves, etc.

---
Driver: between bus infrastructure and framework
In Linux, a driver is always interfacing with:
- a framework that allows the driver to expose the hardware features in a generic way.
- a bus infrastructure, part of the device model, to detect/communicate with the hardware.
Let’s focus on the bus infrastructure for now

---
Device model data structures
The device model is organized around three main data structures:
- The struct bus_type structure, which represent one type of
  bus (USB, PCI, I2C, etc.)
- The struct device_driver structure, which represents one driver capable of handling certain devices on a certain bus.
- The struct device structure, which represents one device connected to a bus
The kernel uses inheritance to create more specialized versions of struct device_driver and struct device for each bus subsystem.

---
The bus driver
- Example: USB. Implemented in drivers/usb/core/
- Creates and registers the bus_type structure
- Provides an API to register and implement adapter drivers
  (here USB controllers), able to detect the connected devices and allowing to communicate with them.
- Provides an API to register and implement device drivers (here USB device drivers)
- Matches the device drivers against the devices detected by the adapter drivers.
- Defines driver and device specific structures, here mainly struct usb_driver and struct usb_interface

---
USB bus example
A single driver for compatible devices, though connected to buses with different controllers.

---
Device drivers (1)
Need to register supported devices to the bus core.
Example: drivers/net/usb/rtl8150.c
static struct usb_device_id rtl8150_table[] = {{ USB_DEVICE(VENDOR_ID_REALTEK, PRODUCT_ID_RTL8150) },{ USB_DEVICE(VENDOR_ID_MELCO, PRODUCT_ID_LUAKTX) },{ USB_DEVICE(VENDOR_ID_MICRONET, PRODUCT_ID_SP128AR) },{ USB_DEVICE(VENDOR_ID_LONGSHINE, PRODUCT_ID_LCS8138TX) },[…]
{}
};
MODULE_DEVICE_TABLE(usb, rtl8150_table);

---
Device drivers (2)
Need to register hooks to manage devices (newly detected or removed ones), as well as to react to power management events (suspend and resume)
static struct usb_driver rtl8150_driver = {
.name = "rtl8150",
.probe = rtl8150_probe,
.disconnect = rtl8150_disconnect,
.id_table = rtl8150_table,
.suspend = rtl8150_suspend,
.resume = rtl8150_resume
};

---
Device drivers (3)
The last step is to register the driver structure to the bus core.
static int __init usb_rtl8150_init(void)
{
return usb_register(&rtl8150_driver);
}
static void __exit usb_rtl8150_exit(void)
{
usb_deregister(&rtl8150_driver);
}
module_init(usb_rtl8150_init);
module_exit(usb_rtl8150_exit);
Note: this code has now been replaced by a shorter module_usb_driver() macro.
Now the bus driver knows the association between the devices and the device driver.

---
Work in the probe() function
probe() is called for each newly matched device
- Initialize the device
- Prepare driver work: allocate a structure for a suitable framework, allocate memory, map I/O memory, register interrupts…
- When everything is ready, register the new device to the framework.

---
At driver loading time
- The USB adapter driver that corresponds to the USB controller registers itself to the USB core
- The rtl8150 USB device driver registers itself to the USB core
- The USB core now knows the association between the vendor/product IDs of rtl8150 and the struct usb_driver structure of this driver

---
When a device is detected

---
The model is recursive
Adapter drivers are device drivers too!

---
Platform devices and drivers
- Want to use the Device Model for devices that are not on buses that can auto-detect devices (very frequent in embedded systems)
- Examples: UARTs, flash memory, LEDs, GPIOs, MMC/SD, Ethernet…
- Solution:
1. Provide a description of devices
2. Manage them through a fake bus: the platform bus.
3. Drive the platform devices

---
Describing non-detectable devices
- Description through a Device Tree (on ARM, PowerPC, ARC…)
- In arch/arm/boot/dts/ on ARM
- Two parts:
  - Device Tree Source (.dts)
    One per board to support in the Linux kernel
    Advantage: no need to write kernel code to support a new board
    (if all devices are supported).
  - Device Tree Source Includes (.dtsi)
    Typically to describe devices on a particular SoC,
    or devices shared between similar SoCs or boards
- Other method for describing non-detectable devices: ACPI
  (on x86 platforms). Not covered here.

---
Declaring a device: .dtsi example
Label
Node name
...
i2c0: i2c@44e0b000 {
compatible = "ti,omap4-i2c";
#address-cells = <1>;
#size-cells = <0>;
ti,hwmods = "i2c1";
reg = <0x44e0b000 0x1000>;
interrupts = <70>;
status = "disabled";
};
...
Compatible drivers
Node
properties
HW register start
address and range
Present but not
used by default
From arch/arm/boot/dts/am33xx.dtsi

---
Instantiating a device: .dts example
&i2c0 {
        pinctrl-names = "default";
        pinctrl-0 = <&i2c0_pins>;
        status = "okay";
        clock-frequency = <400000>;
        tps: tps@24 {
        reg = <0x24>;
        };
        baseboard_eeprom: baseboard_eeprom@50 {
        compatible = "at,24c256";
        reg = <0x50>;
        #address-cells = <1>;
        #size-cells = <1>;
        baseboard_data: baseboard_data@0 {
        reg = <0 0x100>;
        };
        };
};
Pin muxing configuration
(routing to external package pins)
Phandle
(reference
to label)
Enabling this device, otherwise ignored
Node property: frequency
HW register start
address and range
Present but not
used by default
From arch/arm/boot/dts/am335x-boneblue.dts

---
Pin multiplexing
- Modern SoCs have too many hardware blocks compared to physical pins exposed on the chip package.
- Therefore, pins have to be multiplexed
- Pin configurations are defined in the Device Tree
- Correct pin multiplexing is mandatory
  to make a device work from an electronic
  point of view.

---
DT pin definitions
&am33xx_pinmux {
...
i2c0_pins: pinmux_i2c0_pins {
pinctrl-single,pins = <
AM33XX_IOPAD(0x988, PIN_INPUT_PULLUP | MUX_MODE0) /* (C17) I2C0_SDA.I2C0_SDA */
AM33XX_IOPAD(0x98c, PIN_INPUT_PULLUP | MUX_MODE0) /* (C16) I2C0_SCL.I2C0_SCL */
>;
};
…
};
...
&i2c0 {
        pinctrl-names = "default";
        pinctrl-0 = <&i2c0_pins>;
        status = "okay";
        clock-frequency = <400000>;
       ...
};
From arch/arm/boot/dts/am335x-boneblue.dts

---
DT: matching devices and drivers
Platform drivers are matched with platform devices that have the same compatible property.
static const struct of_device_id omap_i2c_of_match[] = {
       {
        .compatible = "ti,omap4-i2c",
        .data = &omap4_pdata,
       },
       {
…
};
…
static struct platform_driver omap_i2c_driver = {
       .probe = omap_i2c_probe,
       .remove = omap_i2c_remove,
       .driver = {
        .name = "omap_i2c",
        .pm = OMAP_I2C_PM_OPS,
        .of_match_table = of_match_ptr(omap_i2c_of_match),
       },
};
From drivers/i2c/busses/i2c-omap.c

---
Usage of the platform bus
Like for physical buses, the platform bus is used by the driver to retrieve information about each device
static int omap_i2c_probe(struct platform_device *pdev)
{
...
struct device_node *node = pdev→dev.of_node;
struct omap_i2c_dev *omap;
...
irq = platform_get_irq(pdev, 0);
…
omap = devm_kzalloc(&pdev->dev, sizeof(struct omap_i2c_dev), GFP_KERNEL);
...
mem = platform_get_resource(pdev, IORESOURCE_MEM, 0);
omap->base = devm_ioremap_resource(&pdev->dev, mem);
u32 freq = 100000; /* default to 100000 Hz */
…
of_property_read_u32(node, "clock-frequency", &freq);
…
return 0;
}
From drivers/i2c/busses/i2c-omap.c

---
Device tree bindings
- Device tree bindings provide a specification of properties that a driver expects in a DT
- Bindings are available in Documentation/devicetree/bindings in kernel sources.
- To know how to set device properties, look for a binding for the same compatible string:
$ git grep “ti,omap4-i2c” Documentation/devicetree/bindings/

---
The I2C bus
- A very commonly used low-speed bus to connect on-board and external devices to the processor.
- Uses only two wires: SDA for the data, SCL for the clock.
- It is a master/slave bus: only the master can initiate transactions, and slaves can only reply to transactions initiated by masters.
- In a Linux system, the I2C controller embedded in the processor is typically the master, controlling the bus.
- Each slave device is identified by a unique I2C address. Each transaction initiated by the master contains this address, which allows the relevant slave to recognize that it should reply to this particular transaction.

---
I2C bus example

---
I2C drivers: probe() function
static int mma7660_probe(struct i2c_client *client,
        const struct i2c_device_id *id)
{
        int ret;
        struct iio_dev *indio_dev;
        struct mma7660_data *data;
        indio_dev = devm_iio_device_alloc(&client->dev, sizeof(*data));
        if (!indio_dev) {
        dev_err(&client->dev, "iio allocation failed!\n");
        return -ENOMEM;
        }
        data = iio_priv(indio_dev);
        data->client = client;
        i2c_set_clientdata(client, indio_dev);
        mutex_init(&data->lock);
        data->mode = MMA7660_MODE_STANDBY;
        indio_dev->dev.parent = &client->dev;
        indio_dev->info = &mma7660_info;
        indio_dev->name = MMA7660_DRIVER_NAME;
        indio_dev->modes = INDIO_DIRECT_MODE;
        indio_dev->channels = mma7660_channels;
        indio_dev->num_channels = ARRAY_SIZE(mma7660_channels);
        ret = mma7660_set_mode(data, MMA7660_MODE_ACTIVE);
        if (ret < 0)
        return ret;
        ret = iio_device_register(indio_dev);
        if (ret < 0) {
        dev_err(&client->dev, "device_register failed\n");
        mma7660_set_mode(data, MMA7660_MODE_STANDBY);
        }
        return ret;
}
device structure for the i2c bus
needed to communicate with the device
Framework (here iio) structure for each device
Per device structure. Used by the driver
to store references to bus and framework structures, plus its own data (locks, wait queues, etc.)
Allocation of the framework, structure. This structure also contains the per device structure (data)
Reference to the bus structure stored in the framework structure.
Reference to the framework structure stored in the bus structure.
Enabling the device (i2c reading and writing)
Register a new framework device when everything is ready (device now accessible in user-space)
Disabling the device in case of failure
From drivers/iio/accel/mma7660.c

---
I2C drivers: remove() function
Same i2c device structure as in probe()
sstatic int mma7660_remove(struct i2c_client *client)
{
        struct iio_dev *indio_dev = i2c_get_clientdata(client);
        iio_device_unregister(indio_dev);
        return mma7660_set_mode(iio_priv(indio_dev),	MMA7660_MODE_STANDBY);
}
Get back the framework structure.
Needed to unregister the framework
device from the system
Unregister the framework
device from the system
Now that user-space can’t access the device any more, disable the device.
From drivers/iio/accel/mma7660.c

---
I2C driver registration
static const struct i2c_device_id mma7660_i2c_id[] = {
        {"mma7660", 0},
        {}
};
MODULE_DEVICE_TABLE(i2c, mma7660_i2c_id);
static const struct of_device_id mma7660_of_match[] = {
        { .compatible = "fsl,mma7660" },
        { }
};
MODULE_DEVICE_TABLE(of, mma7660_of_match);
static const struct acpi_device_id mma7660_acpi_id[] = {
        {"MMA7660", 0},
        {}
};
MODULE_DEVICE_TABLE(acpi, mma7660_acpi_id);
static struct i2c_driver mma7660_driver = {
        .driver = {
        .name = "mma7660",
        .pm = MMA7660_PM_OPS,
        .of_match_table = mma7660_of_match,
        .acpi_match_table = ACPI_PTR(mma7660_acpi_id),
        },
        .probe = mma7660_probe,
        .remove = mma7660_remove,
        .id_table = mma7660_i2c_id,
};
module_i2c_driver(mma7660_driver);
Matching by name (mandatory for I2C)
Matching by compatible property (for DT)
Matching by ACPI ID (for ACPI systems - x86)
From drivers/iio/accel/mma7660.c

---
Raw API for I2C communication
The most basic API to communicate with the I2C device provides functions to either send or receive data:
- int i2c_master_send(struct i2c_client *client, const char *buf, int count);
  Sends the contents of buf to the client (slave).
- int i2c_master_recv(struct i2c_client *client, char *buf, int count);
  Receives count bytes from the client (slave), and store them into buf.
This API is sufficient for simple needs

---
smbus API for I2C communication
SMBus is roughly a subset of I2C. Best to use its Linux API so that I2C drivers will work on controllers supporting only SMBus.
s32 i2c_smbus_write_byte_data(const struct i2c_client *client, u8 command, u8 value);
s32 i2c_smbus_read_byte_data(const struct i2c_client *client, u8 command);
s32 i2c_smbus_read_block_data(const struct i2c_client *client, u8 command, u8 *values);
More details in real world drivers and in kernel documentation:
https://www.kernel.org/doc/html/latest/driver-api/i2c.html#c.i2c_smbus_read_byte_data

---
Driver development advise
- Look for code for devices similar to yours
- Read the code.
  You can use Elixir (https://elixir.bootlin.com/)
- Always read code from the bottom up. You see the big picture first, and then progressively how the details are implemented.

---
Further reading
- Bootlin’s kernel and driver development training materials for full details
  https://bootlin.com/training/kernel/
- Device Tree for Dummies presentation
  Thomas Petazzoni (Apr. 2014)
  http://j.mp/1jQU6NR
- Kernel documentation on I2C
  https://www.kernel.org/doc/html/latest/driver-api/i2c.html

---
Questions?

---
Thank you!